## Slide 1: Scoliosis visualization using ultrasound data
Ben Church

## Slide 2: Contents
Background
Landmark-based visualization
Automatic landmark generation
Full workflow
Discussion and conclusions

## Slide 3: Background - Scoliosis
Pathologic spinal curvature in 3D
Usually diagnosed in adolescence
Curvature progresses with growth

## Slide 4: Background - Assessment
Progression requires monitoring
Cobb angle is the standard measure of scoliotic severity
Cobb angle is measured with X-ray

## Slide 5: Background – Assessment
Patient-specific treatment requires 3D assessment
CT or MRI may be used for treatment decisions
Cannot be used for regular assessment

## Slide 6: Background - Ultrasound
Radiation-free, inexpensive, and accessible
Can measure curvature using skeletal landmarks

## Slide 7: Background - Ultrasound
Scoliosis assessment can benefit from 3D patient-specific spinal visualizations generated from ultrasound data

## Slide 8: Visualization
3D spinal visualizations can be produced by warping a healthy-shaped model to patient skeletal landmarks

## Slide 9: Visualization – Registration
Thin-plate spline registration produces deformed spaces by interpolating transforms between source and target landmarks

## Slide 10: Visualization – Registration
Thin-plate spline requires landmarks to constrain deformation
Transverse processes alone lack anterior-posterior distribution

## Slide 11: Visualization – Registration
Direction of vertebral bodies is computed from transverse process locations
Anchor point is added to each natural landmark to constrain spline

## Slide 12: Visualization – Results
Distance maps give overall impression of visualization accuracy.

## Slide 13: Landmark generation
Manual landmark identification is the most time-consuming step of proposed visualization method
Automatically generating landmark from ultrasound could substantially reduce operator interaction

## Slide 14: Landmark generation – k-means
Bone segmentations can be reduced to landmark sets with k-means algorithm.

## Slide 15: Landmark generation – Defects
Landmarks from k-means may have several defects:
Multiple points on a single landmark
Missing points on landmarks
Incorrectly placed points

## Slide 16: Landmark generation – Defects

## Slide 17: Full workflow
Automatic landmark generation
Bone segmentation
Landmark generation
Landmark set repair
Scoliosis visualization
Healthy-shaped surface and landmarks
Thin-plate spline registration
Transverse process locations
Tracked ultrasound scan
Patient-specific 3D surface visualization

## Slide 18: Full workflow

## Slide 19: Discussion and conclusions
Combination of presented methods bridges gap between ultrasound and 3D visualization
More validation required, depending on application
Method may see modular improvements

## Slide 20: Thank you!
Questions?

## Slide 21: Background – X-ray
X-ray uses ionizing radiation
X-ray assessment is limited to planar views

## Slide 22: Visualization - Overview

## Slide 23: Visualization – Healthy model
Healthy-shaped model consists of landmarks corresponding to patients’ and a surface to be warped

## Slide 24: Visualization - Landmarks
Transverse processes were chosen as landmarks for suitability with ultrasound

## Slide 25: Visualization – Results
Visualizations were generated from 16 scoliotic patients’ transverse process locations
Accuracy of visualizations was assessed by comparing to CT ground-truth

## Slide 26: Visualization – Results
Hausdorff distances and Dice coefficient describe accuracy quantitatively.
Patient # | Maximum Hausdorff (mm) | Average Hausdorff (mm) | Dice coefficient
1 | 16.3 | 2.2 | 0.63
2 | 19.7 | 2.5 | 0.63
3 | 20.0 | 2.0 | 0.63
4 | 13.1 | 2.3 | 0.59
5 | 16.3 | 2.5 | 0.58
6 | 17.9 | 2.5 | 0.57
7 | 16.0 | 2.4 | 0.59
8 | 15.1 | 2.9 | 0.53
9 | 11.4 | 2.0 | 0.69
10 | 9.4 | 1.7 | 0.69
11 | 17.1 | 2.4 | 0.57
12 | 14.0 | 2.4 | 0.64
13 | 14.8 | 2.7 | 0.53
14 | 14.6 | 2.5 | 0.61
15 | 13.3 | 2.0 | 0.63
16 | 15.3 | 1.8 | 0.58
Average | 15.3 | 2.3 | 0.61
Standard deviation | 2.7 | 0.3 | 0.04

## Slide 27: Visualization – Discussion
Visualizations capture 3D deformation
Inaccuracies mainly at boundaries and vertebral bodies

## Slide 28: Visualization – Discussion
Method has not been validated for navigation
Method has been used in work by Baum et al.

## Slide 29: Landmark generation - Segmentation
A new PLUS tool was used to segment bones from spinal ultrasound

## Slide 30: Landmark generation - Segmentation
The method checks for acoustic shadows to determine presence of bone

## Slide 31: Landmark generation - Segmentation
The segmentation can be rendered as a surface

## Slide 32: Landmark generation – Right-left
Defects are tested for and repaired side-wise
Points must be identified as belonging to right or left side of spine

## Slide 33: Landmark generation – Right-left
Un-normalized left-right landmark distribution not immediately separable
Curvature can prevent linear separation

## Slide 34: Landmark generation – Right-left
k-means classifies points landmarks window by window

## Slide 35: Landmark generation – Duplicates
Multiple points placed on a single landmark are identified by angles between inter-point vectors

## Slide 36: Landmark generation – Duplicates

## Slide 37: Landmark generation – Omissions
Inter-landmark interval length are compared locally and globally
Unusually long interval lengths indicate omissions

## Slide 38: Landmark generation – Omissions

## Slide 39: Landmark generation – Omissions

## Slide 40: Landmark generation – Omissions

## Slide 41: Landmark generation – Outliers
Outliers are identified similarly to duplicates, but as individual points

## Slide 42: Landmark generation – Outliers

## Slide 43: Landmark generation – Outliers

## Slide 44: Landmark generation – Boundaries
Defects are corrected by interpolation
Overhanging points must be removed from both sides

## Slide 45: Full workflow
5 volunteers were scanned
Scans were segmented
Landmarks were generated from segmentations
Visualizations were produced from landmarks

## Slide 46: Full workflow

## Slide 47: Full workflow

## Slide 48: Full workflow

## Slide 49: Full workflow

## Slide 50: Full workflow