## Slide 1: Scoliosis visualization using ultrasound data
Ben Church

## Slide 2: Overview
Ch. 4: Landmark generation from ultrasound
  Ch. 4.2: Segmentation under-sampling
  Ch. 4.3: Landmark refinement
  Ch. 4.5: Full workflow test cases
Ch. 3: Landmark registration for visualization
  Ch. 3.4: Registration constraint
  Ch. 3.5: Validation
Ch. 2: Motivation
  Ch. 2.2.1: Scoliosis assessment with X-ray
  Ch. 2.3: Scoliosis assessment with ultrasound

## Slide 3: Ch. 2.2.1: Scoliosis assessment with X-ray
Developmentally progressive curvature must be monitored.
Standard assessment metric is the Cobb angle.
X-ray imaging is hazardous and limited [Doody2000], [Presciutti2014].

## Slide 4: Ch. 2.3: Scoliosis assessment with ultrasound
Tracked ultrasound can be used to locate skeletal landmarks [Purnama2010], [Brudfors2015].
Curvature can be measured from landmarks [Chen2013], [Ungi2014].

## Slide 5: Ch. 2: Motivation Scoliosis visualization
Patient-specific treatments require 3D assessment [Kalichman2016].
Ultrasound assessment methods lack 3D visualization.

## Slide 6: Ch. 3: Landmark registration for visualization
A landmark-based thin-plate spline registration can be used to warp a healthy-shaped model onto patient anatomy [Church2017a].

## Slide 7: Ch. 3.4: Registration constraint
Algorithmic supplementation of landmarks with anchor points required to constrain warping

## Slide 8: Ch. 3.5: Validation
dfass

## Slide 9: Ch. 4: Landmark generation from ultrasound
Manual landmark identification is the most time-consuming step of proposed visualization method.
Automatically generating landmark from ultrasound could substantially reduce operator interaction.

## Slide 10: Ch. 4.2: Segmentation under-sampling
Bone segmentations can be reduced to landmark sets with k-means algorithm.

## Slide 11: Ch. 4.3: Landmark refinement
Landmarks from k-means may have several defects:
Multiple points on a single landmark
Missing points on landmarks
Incorrectly placed points

## Slide 12: Ch. 4.5: Full workflow test cases

## Slide 13: Ch. 4.5: Full workflow test cases

## Slide 14: Conclusions
Method for generating 3D patient-specific spinal visualizations from ultrasound-accessible landmarks developed and validated.
Landmark locations can be estimated automatically and refined with modest user interaction.
Combination of presented methods bridges gap between ultrasound and 3D visualization.

## Slide 15: Ongoing work
Application-specific validation [Baum2018]
Improving segmentation method
Investigating surface registration method

## Slide 16: Posters and publications
B. Church, A. Lasso, C. Schlenger, D. P. Borschneck, P. Mousavi, G. Fichtinger and T. Ungi, "Visualization of scoliotic spine using ultrasound-accessible skeletal landmarks," in Proceedings of SPIE, Orlando, 2017. [Church2017a]
B. Church, A. Lasso, C. Schlenger, D. P. Borschneck, P. Mousavi, G. Fichtinger, T. Ungi, “Scoliosis visualization using transverse process landmarks,” poster at ImNO 2017. [Church2017b]
C. Pinter, B. Travers, Z. Baum, S. Kamali, T. Ungi, A. Lasso, B. Church and G. Fichtinger, “Real-time transverse process detection in ultrasound,” in Proceedings of SPIE, Houston, 2018. [Pinter2018]
Z. Baum, T. Ungi, A. Lasso, B. Church, C. Schlenger, G. Fichtinger, "Visual aid for identifying vertebral landmarks in ultrasound," in Proceedings of SPIE, Houston, 2018. [Baum2018]

## Slide 17: Thank you!
Questions?

## Slide 18: References
[Baum2018] Z. Baum, T. Ungi, A. Lasso, B. Church, C. Schlenger, G. Fichtinger, "Visual aid for identifying vertebral landmarks in ultrasound ," in Proceedings of SPIE, Houston, 2018.
[Brudfors2015] M. Brudfors, A. Seitel, A. Rasoulian, A. Lasso, V. A. Lessoway, J. Osborn, A. Maki, Robert N. Rohling, P. Abolmaesumi, “Towards real-time, tracker-less 3D ultrasound guidance for spine anaesthesia,” Int J CARS, vol. 10, p. 855-865, 2015.
[Chen2013] W. Chen, E. H. M. Lou, P. Q. Zhang, L. H. Le and D. Hill, "Reliability of assessing the coronal curvature of children with scoliosis by using ultrasound images," J Child Orthop, vol. 7, p. 521–529, 2013.
[Church2017a] B. Church, A. Lasso, C. Schlenger, D. P. Borschneck, P. Mousavi, G. Fichtinger and T. Ungi, “Visualization of scoliotic spine using ultrasound-accessible skeletal landmarks," in Proceedings of SPIE, Orlando, 2017.
[Church2017b] B. Church, A. Lasso, C. Schlenger, D. P. Borschneck, P. Mousavi, G. Fichtinger, T. Ungi, “Scoliosis visualization using transverse process landmarks,” poster at ImNO 2017.
[Doody2000] M. M. Doody, J. E. Lonstein, M. Stovall, D. G. Hacker, N. Luckyanov and C. E. Land, "Breast Cancer Mortality After Diagnostic Radiography," SPINE, vol. 25, no. 16, p. 2052–2063, 2000.
[Kalichman2016] L. Kalichman, L. Kendelker and T. Bezalel, "Bracing and exercise-based treatment for idiopathic scoliosis," Journal of Bodywork & Movement Therapies, vol. 20, pp. 56-64, 2016.
[Pinter2018] C. Pinter, B. Travers, Z. Baum, S. Kamali, T. Ungi, A. Lasso, B. Church and G. Fichtinger, “Real-time transverse process detection in ultrasound,” in Proceedings of SPIE, Houston, 2018.
[Presciutti2014] S. M. Presciutti, T. Karukanda and M. Lee, "Management decisions for adolescent idiopathic scoliosis significantly affect patient radiation exposure," The Spine Journal, vol. 14, pp. 1984-1990, 2014.
[Purnama2010] K. E. Purnama, M. H. F. Wilkinson, A. G. Veldhuizen, P. M. A. v. Ooijen, J. Lubbers, J. G. Burgerhof, T. A. Sardjono and G. J. Verkerke, "A framework for human spine imaging using a freehand 3D ultrasound system," Technology and Health Care, vol. 18, p. 1–17, 2010.
[Ungi2014] T. Ungi, F. King, M. Kempston, Z. Keri, A. Lasso, P. Mousavi, J. Rudan, D. P. Borschneck and G. Fichtinger, "Spinal Curvature Measurements by Tracked Ultrasound Snapshots," Ultrasound in Med. & Biol., vol. 40, no. 2, pp. 447-454, 2014.

## Slide 19: Background – X-ray
X-ray uses ionizing radiation
X-ray assessment is limited to planar views

## Slide 20: Visualization - Overview

## Slide 21: Visualization – Healthy model
Healthy-shaped model consists of landmarks corresponding to patients’ and a surface to be warped

## Slide 22: Visualization - Landmarks
Transverse processes were chosen as landmarks for suitability with ultrasound

## Slide 23: Visualization – Results
Visualizations were generated from 16 scoliotic patients’ transverse process locations
Accuracy of visualizations was assessed by comparing to CT ground-truth

## Slide 24: Visualization – Results
Hausdorff distances and Dice coefficient describe accuracy quantitatively.
Patient # | Maximum Hausdorff (mm) | Average Hausdorff (mm) | Dice coefficient
1 | 16.3 | 2.2 | 0.63
2 | 19.7 | 2.5 | 0.63
3 | 20.0 | 2.0 | 0.63
4 | 13.1 | 2.3 | 0.59
5 | 16.3 | 2.5 | 0.58
6 | 17.9 | 2.5 | 0.57
7 | 16.0 | 2.4 | 0.59
8 | 15.1 | 2.9 | 0.53
9 | 11.4 | 2.0 | 0.69
10 | 9.4 | 1.7 | 0.69
11 | 17.1 | 2.4 | 0.57
12 | 14.0 | 2.4 | 0.64
13 | 14.8 | 2.7 | 0.53
14 | 14.6 | 2.5 | 0.61
15 | 13.3 | 2.0 | 0.63
16 | 15.3 | 1.8 | 0.58
Average | 15.3 | 2.3 | 0.61
Standard deviation | 2.7 | 0.3 | 0.04

## Slide 25: Visualization – Discussion
Visualizations capture 3D deformation
Inaccuracies mainly at boundaries and vertebral bodies

## Slide 26: Visualization – Discussion
Method has not been validated for navigation
Method has been used in work by Baum et al.

## Slide 27: Landmark generation - Segmentation
A new PLUS tool was used to segment bones from spinal ultrasound

## Slide 28: Landmark generation - Segmentation
The method checks for acoustic shadows to determine presence of bone

## Slide 29: Landmark generation - Segmentation
The segmentation can be rendered as a surface

## Slide 30: Landmark generation – Right-left
Defects are tested for and repaired side-wise
Points must be identified as belonging to right or left side of spine

## Slide 31: Landmark generation – Right-left
Un-normalized left-right landmark distribution not immediately separable
Curvature can prevent linear separation

## Slide 32: Landmark generation – Right-left
k-means classifies points landmarks window by window

## Slide 33: Landmark generation – Duplicates
Multiple points placed on a single landmark are identified by angles between inter-point vectors

## Slide 34: Landmark generation – Duplicates

## Slide 35: Landmark generation – Omissions
Inter-landmark interval length are compared locally and globally
Unusually long interval lengths indicate omissions

## Slide 36: Landmark generation – Omissions

## Slide 37: Landmark generation – Omissions

## Slide 38: Landmark generation – Omissions

## Slide 39: Landmark generation – Outliers
Outliers are identified similarly to duplicates, but as individual points

## Slide 40: Landmark generation – Outliers

## Slide 41: Landmark generation – Outliers

## Slide 42: Landmark generation – Boundaries
Defects are corrected by interpolation
Overhanging points must be removed from both sides

## Slide 43: Full workflow
5 volunteers were scanned
Scans were segmented
Landmarks were generated from segmentations
Visualizations were produced from landmarks

## Slide 44: Full workflow

## Slide 45: Full workflow

## Slide 46: Full workflow

## Slide 47: Full workflow

## Slide 48: Full workflow